## Slide 1: Library anomaly detection using Deep learning
Srinivas Bodapati, Vidya Sagar Reddy Gopala

## Slide 2: Motivation
Standard cell characterization data at multiple process, voltage and temperature (PVT) runs into Terabytes.
  Validation becomes a big data problem
Library collateral/data quality is essential to SoC design.
  Collateral error(s) may cause design failure
  Cost of fixing library data is expensive if errors found late in the design cycle
  Negatively Impacts project schedules.
Need scalable validation solution that is
  Accurate, fast (quick turn around time (TAT)), enables easy debug
Notes: run time trade off limitations in using traditional QA or validation tools.
No adaptable trend based validation exists for library characterization data. Or no tool captures the trends in Characterization database to detect anomalies.
Improve characterization library data quality using predictive analytics.

## Slide 3: Proposed Solution
Developed new deep learning based library validation infrastructure with Web-UI that is fast, accurate and enables easier debug of collateral.
  It allows automatic root cause analysis and captures anomalies and trends.
Enables detection of anomalies in library characterization
  Strange/erroneous char data due to any reason
  Invalid trends
  Identifies the exact cell/timing-arc and char point that

## Slide 4: Library Validation Architecture

## Slide 5: Stage 1: Big data processing of library data
Terabytes of Library Characterization data is converted to Structured data with any distributed computing Frameworks.
Parsed library data is converted into JSON documents for further analytics.
For each measurement, features are extracted for model inputs.
Extracted features include library, topology, cell and arc information.
Data-frames of input features are fed to neural network to predict required measurements such as delay, slew, capacitance and more.
Neural network
Characterization data (.lib)
Converting characterization data to structured documents
Structured JSON documents for analytics
Feature extraction
Stage 1
Notes: Bullet instead of points.
Animation for NN part

## Slide 6: Stage 2: Deep Neural Net Architecture
Categorical features
Continuous features
Embedding layer
Flatten and concat
‘4’ Hidden layers with dropouts
Linear activated Output layer
Predicted measurement
Stage 2
(16x1)
(16x50)
(1x1) + (2x8)
(1x817)
(1x512)
(1x64)
Activation: Relu (Hidden layers)
Linear (O/P layer)
Dropouts used.
Notes: Reduce bullet points content
Embedding's[2] are used to capture the relationship between categorical features such as cell names, pin names, direction, arc etc.,
Continuous features are normalized and directly fed to the neural net.
Output of embedding layer is flattened and concatenated with continuous features. Concatenated output it then followed by few hidden layers.
To avoid overfitting dropouts and regularization techniques are used.
‘relu’ activation is used for hidden layers, wherein linear for output layer.

## Slide 7: Features and embedding
Topology
Cell type
Height
. . .
. . .
Cell name
Pin name
Related pin
Slope
load
Cell area
Embedding layer
Flatten and concat
NN
Embedding layer greatly improves the modelling.
  Maps categorical variables to vector space.
  Vector is adjusted with the training.
Categorical inputs are encoded, padded and fed to embedding layer.
Continuous features are concatenated with flattened output of embedding.
Embedding layer is followed by hidden & output layers.
Here in the block,
  ‘n’ : number of unique categories (size of vocab)
  ’50’: Standard size of vector good enough for multi-dimensional grouping.
(16x1)
(16xnx50)
(1x1)
(1x8)
(1x8)
(1x817)
Notes: Example with animation in next slide

## Slide 8: Embedding layer explained
Here for example, let us consider 1 categorical input (topology) with 4 unique categories and vector size of 50 for each unique category. Let us assume inv, and, or & nand as unique types in category called topology.
A embedding layer of size 1X4X50 is build and trained to group categories closer on multi-dimensional space.
Inv [0 0.1 . . . . . . . . . . . . 1] (1x50)
And [0 0.3 . . . . . . . . . . .0.9] (1x50)
Or [0 0.5 . . . . . . . . . . .0.1] (1x50)
Nand [0 0.9 . . . . . . . . . . .1.1] (1x50)
Topology (inv)
(1x1)
(4x50)
Cell area Slope Load Concatenated and flattened embedding vector
NN
Inputs to the neural network

## Slide 9: Stage 3: Anomaly detection and report generation
High leverage points
Algorithm derived from Cook’s distance
Long tail of the error distribution based on quantile (absolute and percentile error)
Quantile based
Possible Anomalies
A linear model is fit sweeping load and slope to detect R2 and trend/slope
if:
trend/slope == ‘-ve’
||
R2 score < 0.9 (reference)
Yes
No
Anomalies
Discard
Fitting the model over each anomaly
Append it to list of anomalies
Database of arcs with actual data, predicted data, abs error and percentile error
Visual insight of anomalies with Web-UI
Stage 3
Web-UI is developed to visualize anomalies and navigate through characterization database to debug the anomaly easily.
Anomaly characterization is difficult as there are very few anomalies, so we need to filter true outliers after prediction stage.

## Slide 10: Results
Detected anomaly!
Notes: To provide easy debug interface to the users, a web-UI is developed with multi-level navigation based on lib hierarchy.
Top level web page summarizes data and error distribution. For each liberty, visualizations are provided to give a visual insight to the user.
As shown in the figure;
  Fig (a): Histogram distribution of measurement data depicting the wide spread distribution of measurement.
  Fig (b): Histogram distribution of measurement error helping user to estimate the sigma deviation, long tail and error distribution.
  Fig (c): Number of anomalies detected in each topology.
  Fig (d): Contour distribution of anomaly across l
  oad/slope table. This plot helps in understanding bad load/slope combination across the entire library causing the anomalies.
Followed by table of hyperlinks, helping us to navigate to anomalous topology of interest. This way, user is given a chance to debug anomalies hierarchically (library/family/cell/measurement).

## Slide 11: Results (Contd..)
Bad load/slope combination
Histogram profiling of measurement across the library
Histogram distribution of error
Number of anomalies across the topologies
Contour distribution of error across load/slope

## Slide 12: Summary
Presented a deep learning based advanced validation tool to capture trends over entire library.
  Statistical anomaly methods used in detecting anomalies.
  More robust than standard threshold based outliers.
Detects anomalies which do not follow the trend, source of anomaly could be
  Simulation failures/errors, lsf issues
  Incorrect configuration/setup
Adaptable trend based validation not susceptible to technology changes like transistor models, interconnect models etc.
  Traditional methods require thresholds that may change with technology changes.
Identifies true anomalies and reduces false positives compared to traditional threshold based methods.
  Traditional methods require aggressive thresholds else they generate millions of violations.
Identifies cells/arcs with bad trends and navigates designer to exact source of the anomalies.
Deep learning validation QA captures the trend and correlation across the library and cells. Wherein, traditional methods only captures local trends of the arc.
Notes: References:
Zaharia, Matei, et al. "Apache spark: a unified engine for big data processing." Communications of the ACM 59.11 (2016): 56-65.
https://towardsdatascience.com/deep-learning-structured-data-8d6a278f3088
Chatterjee, Samprit, and Ali S. Hadi. Sensitivity analysis in linear regression. Vol. 327. John Wiley & Sons, 2009.