## Slide 1: Novel Approach in Differential CDC Analysis of Parameterized IP
Ashish Soni, Anubhav Arora (ST Microelectronics, India)
Amit Goldie, Navneet Kumar Chaurasia (Synopsys, India)
Conventional Flow
Results of Proposed Solution
Abstract
It’s fairly common for SoCs, out their today, to support lots of features which are fairly complex and divergent in nature. This leads to integration of various different IPs in SoCs. In most of these IPs new features are coded keeping in mind use case of features – hence parameters are needed in RTL. Each parameter or different values of parameters branch out complex pieces of code thereby increasing complexity of the IP. In this paper we proposing a flow using which designers can easily and effectively figure out the complete parametrization impact on CDC closure. They can now reliably reuse the effort and compare the outputs of other configurations and not rely on heuristics solely.
Conclusion
The proposed approach allows designers to analyze the CDC violations for various parameter configurations easily by prioritizing the RTL fixes and application of waivers from other parameter configuration runs which are not based on heuristics.
Earlier without the differential analysis, designer spends a lot of time analyzing the violations individually for each configuration run without re-using or re-applying the analysis effort of the previous configuration runs. Now, by using this approach, designer can apply a common effort on analyzing and cleaning multiple configurations. Hence analysis time of cleaning the CDC violations is significantly reduced.
Acknowledgement
For Cfg1
  Designer creates setup for cfg1
  Analyzes reports for cfg1
  Gets CDC Clean IP for cfg1
Single Parameter
Configuration
Constraints
RTL
cfg1_param.tcl
cfg1_cons.sgdc
Reports on Various Violations
Applying Waivers
SpyGlass
Setup Phase
Analysis Phase
CDC Clean IP for 1st Cfg
Effort to clean 1st Configuration
Effort to clean
Nth Configuration
For CfgN
  Designer creates setup for cfgN
  Analyzes reports for cfgN
  Gets Clean IP for cfgN
Independent Effort applied on N.. configurations
Multifold Increase in Analysis Time
Leads to
Single Parameter
Configuration
Constraints
RTL
cfgN_param.tcl
cfgN_cons.sgdc
Reports on Various Violations
Applying Waivers
SpyGlass
Setup Phase
Analysis Phase
CDC Clean IP for Nth Cfg
New Proposed Flow
Multiple Parameter Configurations
Multiple Constraints
RTL
cfg2_param.tcl
cfg1_param.tcl
cfg2_cons.sgdc
cfg1_cons.sgdc
Reports cfg1
Reports cfg2
Reports cfgN
analyse_data
Console_dump
SpyGlass GUI
SpyGlass
Setup Phase
Import Phase
Differential
Analysis Phase
Export Phase
cfgN_param.tcl
cfgN_cons.sgdc
Setup Phase
Designer provides parameters, constraints and waivers (if any) for all requisite configurations and runs SpyGlass to write out various reports used in Import phase.
Import Phase
In this phase, proposed solution parses through the violation reports and the user applied waiver files.
Differential Analysis Phase
In this phase, solution performs in depth differential analysis on requisite configurations and generate results.
Export Phase
In this phase, various analysis reports are written for user to be imported in SpyGlass tool for debug in GUI mode.
Reduced Effort in Cleaning Multiple Cfgs
c
config_N
c1
uN
u2
c2
u1
u0
Errors common across all configurations
Common errors could exist between few configurations but not common for all
Unique Errors
config_2
config_1
config_0
c3
param_1
param_2
param_3
param_N
config_N
config_2
config_1
config_0
w
x
y
z
b
a
c
b
p
q
r
n
l
m
m
o
Displays Parameters which have differences across configurations
config_2
config_1
config_0
Total
Displayed
Waived
T2
T1
T0
D2
W2
D1
D0
W1
--
Displays the total number of violations
(T) = Displayed (D) + Waived errors (W)
c3